## Slide 1: Configuration Space, Task Space, Workspace and Introduction to ROS
CS 6301 Special Topics: Introduction to Robot Manipulation and Navigation
Professor Yu Xiang
The University of Texas at Dallas

## Slide 2: Configuration Space of a Robot
The configuration of a robot is a complete specification of the position of every point of the robot.
The minimum number n of real-valued coordinates needed to represent the configuration is the number of degrees of freedom (DOF) of the robot.
The n-dimensional space containing all possible configurations of the robot is called the configuration space (C-space).
The configuration of a robot is represented by a point in its C-space.
4 revolute joints
4 DOFs

## Slide 3: Configuration Space Topology
Configuration specifies the position of a robot
For a robot with n joints, the configuration is a vector in
  C-space
Joints may have limits, upper bound and lower bound
Topology: shape of the space
  Consider all the feasible points in the configuration space

## Slide 4: Configuration Space Topology
n-dimensional Euclidean space
n-dimensional sphere in a (n+1)-dimensional Euclidean space
  Two-dimensional surface of a sphere in three-dimensional space
The C-space can have different representations, but its shape is the same
  A point on a unit circle can have two representations
  angle , or coordinates (x, y)

## Slide 5: Configuration Space Topology
C-space as Cartesian product (all ordered pairs)
  A rigid body in the plane
  A PR robot (Prismatic-Revolute)
    Ignore joint limits
  A 2R robot
n-dimensional surface of a torus in an (n+1)-dimensional space
sample representation

## Slide 6: Configuration Space Topology
C-space of a planar rigid body (chassis of a mobile robot) with a 2R robot arm
C-space of a rigid body in 3D space
  3D translation
  3D rotation

## Slide 7: Task Space
The task space is a space in which the robot’s task can be naturally expressed
Task examples
  Draw on a piece of paper:
  Manipulate a rigid body: C-space of the rigid body
Task space is driven by the task, independently of the robot

## Slide 8: Workspace
The workspace is a specification of the configurations that the end-effector of the robot can reach.
Depends on the robot structure, independent of the task
a planar 2R open chain
a planar 3R open chain
a spherical 2R open chain

## Slide 9: SCARA Robot
End-effector configuration
Task space
Workspace
  Reachable

## Slide 10: A 6R Robot
A spray-painting robot
End-effector configuration
Task space
Workspace
  Reachable
spray nozzle
Cartesian position of the nozzle
Spherical coordinates to describe
the direction in which the nozzle is pointing

## Slide 11
https://www.rnaautomation.com/case-study/robotic-spray-booth/

## Slide 12: Robot Programming
Sensing
  How to receive data from sensors on the robot?
  RGB image, depth image, lidar scan, odometry, joint state
Computation
  Use the sensor data for computation
  Object recognition, motion planning, compute control command, etc.
Control
  How to send the control command to the robot?

## Slide 13: Robot Operating System (ROS)
ROS is a set of software libraries and tools that can be used to build robot applications
  Drivers, algorithms, developer tools, etc.
Goal of ROS: support code reuse in robotics research and development
Operating systems: Unix-based platforms (Ubuntu)
https://www.ros.org/
https://wiki.ros.org/

## Slide 14: Robot Operating System (ROS)
https://www.ros.org/

## Slide 15: ROS Computation Graph
The computation graph is the peer-to-peer network of ROS processes that are processing data together
Computation graph concepts
  Nodes: processes that perform computation
  ROS Master: provides name registration and lookup, nodes can find each other via ROS master
  Messages: nodes communicate by passing messages, a data structure with type fields (integer, floating, arrays, etc.)

## Slide 16: ROS Message Example

## Slide 17: ROS Computation Graph
Topics: a node publishes messages to a topic. The topic is the name to identify the content of the message
Node: Head camera
Topic: /rgb_image
Node: Object detection
Message: sensor_msgs/Image

## Slide 18: ROS Computation Graph
Service: request and reply interactions
Node: Motion Planner
Node: Arm Controller
Service: FollowJointTrajectory

## Slide 19: ROS Computation Graph
ROS bags
  A format for saving and playing back ROS message data
  We can save sensor data into a ros bag, and use it for development

## Slide 20: Using ROS
Ubuntu users
Mac users
Windows users

## Slide 21: Using ROS with Ubuntu
Install ROS http://wiki.ros.org/noetic/Installation/Ubuntu

## Slide 22: Using ROS with Mac
Download the Ubuntu 20.04 .iso from https://cdimage.ubuntu.com/releases/focal/release/ (pick arm or amd based on if you have m1 or intel mac)
Download UTM from https://mac.getutm.app/
Follow this video to install the ubuntu image in Mac https://www.youtube.com/watch?v=1WWj6qoWhJw
Use ROS as in Ubuntu

## Slide 23: Docker: Using ROS with Windows
An open platform that enables you to separate your applications from your infrastructure
Container
  A lightweight environment that contains everything to run an application
  A container is a runnable instance of an image
Image
  A read-only template with instructions for creating a docker container

## Slide 24: Ubuntu in Docker
Download the ubuntu docker image https://hub.docker.com/_/ubuntu
docker pull ubuntu:20.04
Command
Docker image name
Docker image tag

## Slide 25: Docker
Run an ubuntu container
You need to have an ubuntu image locally, if not, the command will pull an ubuntu image as by docker pull ubuntu
Docker creates a new container as though you had run docker container create
Docker starts the container and execute /bin/bash
-i, -t the container is running interactively and attached to your terminal
When exit, the container stops but is not removed
docker run -i -t ubuntu:20.04 /bin/bash

## Slide 26: ROS in Docker
Install Docker Desktop https://docs.docker.com/get-docker/
Start the Docker Desktop
Ubuntu images https://hub.docker.com/_/ubuntu
Run command “docker run –i –t ubuntu:20.04 /bin/bash”
No need to use sudo in docker, do an “apt update” first
Install ROS http://wiki.ros.org/noetic/Installation/Ubuntu
Install terminator https://manpages.ubuntu.com/manpages/bionic/en/man1/terminator.1.html

## Slide 27: ROS in Docker
Install X server
  Windows: VcXsrv Windows X Server https://sourceforge.net/projects/vcxsrv/
  Mac: Xquartz https://www.xquartz.org/
Start the X server
Check IP address
In Ubuntu terminal
Export DISPLAY=my_ip:0.0
https://medium.com/@potatowagon/how-to-use-gui-apps-in-linux-docker-container-from-windows-host-485d3e1c64a3

## Slide 28: ROS in Docker
Test ROS installation
In one terminator terminal, start roscore
  source /opt/ros/noetic/setup.bash
  roscore
In another terminator terminal, start rviz
  source /opt/ros/noetic/setup.bash
  rosrun rviz rviz

## Slide 29: Commit Your Docker Image
After you exit the docker container
Run the command “docker container list -a” to see all the containers. Find the container ID of the latest one
Run the command “docker container commit <CONTAINER_ID>”
Run the command “docker image list -a” to see the latest image ID
Run the command “docker image tag <IMAGE_ID> TAG”. Give a name to this image such as “ubuntu:ros”

## Slide 30: ROS in Docker
After install all needed packages, exit
docker container commit CONTAINER_ID
docker image tag <IMAGE_ID> TAG
Useful commands
  docker container list –a
  docker image list -a
The new tagged image will have all the installed packages

## Slide 31: Summary
Task space
Workspace
ROS
Docker

## Slide 32: Further Reading
Chapter 2 in Kevin M. Lynch and Frank C. Park. Modern Robotics: Mechanics, Planning, and Control. 1st Edition, 2017 http://hades.mech.northwestern.edu/images/7/7f/MR.pdf
ROS wiki https://wiki.ros.org/
Docker document https://docs.docker.com/get-started/overview/